## Slide 1: Transistor circuits & FETs
First transistor, 1947, Bell Labs
Week 6

## Slide 2: Art of Electronics (AoE)
Many of the figures and in this ppt are from Horowitz and Hill’s AoE book

## Slide 3: BJT Golden Rules
There are no golden rules … there are many configurations and possibilities with BJTs…
The base-emitter often acts like a diode
  If Vbe < ~0.6V then ic ~ 0 and the transistor is “off”
  If Vbe~0.6-0.7V (forward biased diode), the collector-emitter conducts
  Making Vbe>0.7V will likely destroy the device quickly
If not saturated, ic = hfe * ib = b * ib
The transistor will lower its collector-emitter voltage in order to satisfy (3.) But it can’t go below Vce~ 0.01-0.3V
Like diodes (e.g., LEDs), external components are generally needed to limit base and collector currents at safe (for the device) values
…

## Slide 4: 4 Important 1 transistor circuits
Fixing or floating various terminals gives various circuit properties (and a whole lot to remember and get confused about)
fixed
out
in
out
fixed
fixed
Switch
in
out
fixed
in
Follower
Current source (sink)
Amplifier
out
fixed
fixed

## Slide 5: Switch
  For an NPN, if Vb-Ve ~0.6V and Vc > Ve (by >~0.2V) then
    Ic tries to equal hfeIb where hfe is the transistor’s current gain ~ 100-400 typically
    Typically Ic will saturate at a lower current, limited by the the collector source impedance
    In “cutoff”, Ib “closes” a switch between c and e
    When Vin = high, Vout  0 the voltages invert
    When Iin is high, IL is high, the currents don’t invert
Vin
Vout
b
e
c
RL

## Slide 6: What happens in saturation?
“Transistor man” adjusts a variable resistor that’s a voltage divider with Rc. Once set to its minimum value (R=Vce/ic), it can’t go any lower
ic is now saturated at (Vcc-Vce)/Rc, additional increase in ib cannot increase ic
In saturation, the external collector circuitry (Rc) determines ic, not hfeib.
Rc
Vcc
How do you feel about this model?

## Slide 7: Emitter-follower
Vout = Vin - 0.6V – not very exciting, voltage gain ~1
  Since we’re often interested in time-varying signals:
  dVout/dt = dVin/dt  voltage gain dVout/dVin = 1
But the current gain, Iout/Iin ~hfe
Derivations and more at:
https://en.wikipedia.org/wiki/Common_collector

## Slide 8: Current sources
Compliance is still limited by Re. Can we eliminate it?
Just as constant voltage sources (independent of RL) are very useful, so are constant current sources.
Compliance refers to their ability maintain constant i as RL varies

## Slide 9: Common-emitter amplifier
A current source with resistive load is a voltage source
Vc = Vcc – icRc
ie = Ve/Re ≈ Vb/Re ≈ ic
Vc = Vcc – VbRc / Re
gain = –Rc / Re
Note: This is an inverting amplifier. RE provides negative feedback.

## Slide 10: Important 1 transistor circuits
Fixing or floating various terminals gives various circuit properties (and a whole lot to remember and get confused about)
fixed
out
in
out
fixed
fixed
Switch
in
out
fixed
in
Follower
Current source (sink)
Amplifier
out
fixed
fixed

## Slide 11: Some 2 transistor circuits
One of the goals of learning the “language” of electronics is to recognize circuits as building blocks of increasing complexity
You don’t read a newspaper parsing each letter or word, but instead see sentences, paragraphs, articles, sections – a hierarchy of structure
These 1-transistor circuits are sentences
The following 2 transistor circuits are analogous to paragraphs in circuits …

## Slide 12: Darlington configuration
Darlingtons combine two transistors, often in one physical package
  b = b1 * b2
  Vbe = Vbe1 + Vbe2 ~1.3V
  Switching time is slower
Note: FETs have nearly infinite b

## Slide 13: Current mirrors
Two matched transistors with the same Vbe should have the same ic.
Transistors should be touching (or on the same die) to be at same T
Additional tricks improve mirrors …
or buy a current source IC
(Current mirrors are very common inside ICs)
=(Vcc-.6)/R
R
Iout = IREF
Independent of Vout

## Slide 14: Push-pull output
NPN emitter-follower has low Zout, but can’t sink current
Likewise PNP e-followers can’t source current
So put them together …
input
-15V
Zspeaker~8W

## Slide 15: Differential amplifier
Vout = Gdiff(V+-V-) + ½ GCM(V++V-)
These are the guts (brains?) of a lot of analog electronics because they permit amplifying small voltage differences while rejecting large common signals
Often Vcc and/or Vee are replaced by current sources
FETs in place of Q1 and Q2 can increase the input impedances to >1012 ohms
Don’t try to build these … use integrated circuits that offer overvoltage protection circuits, temperature stability, better linearity, lower noise, etc.
  But being able to recognize them as a single construct or element is helpful in deciphering schematics

## Slide 16
Your comfort level “understanding” these 2-transistor circuits is likely pretty low – and that’s just fine
It will grow as needed
We’ll work through a simple (yet powerful) example later

## Slide 17: BJT summary
Transistors behave distinctly in 3 regimes, “off”, where ib and ic ~ 0, “active”, where ib and ic were related by the transistor’s intrinsic property hfe=ic/ib, and “saturated”, where ic was constant, limited primarily by extrinsic circuit properties (often Vc/Rc)
A simple circuit quantified the current gain, b = hfe=ic/ib, with 2 resistors that both limited and measured ib and ic
The transistor switch only requires a tiny ib (that can through our fingers and body without sensation) to control (turn on and off) an LED (ic)

## Slide 18: ICs are usually better
Integrated circuits usually offer far superior performance to these single transistor circuits, at virtually the same costs
Need an amplifier, use an op-amp, instrumentation amp, …
Need a voltage regulator or current source, look for ICs
  Consider our <$1 LM317 – it has dozens of transistors within it make it more robust, safe, linear, …

## Slide 19: Ebers-Moll
http://en.wikipedia.org/wiki/Ebers-Moll
Ebers-Moll is a more accurate
model of the large signal
characteristics of a bipolar transistor
Isat is a messy function of T, etc., so this is even uglier…
Early Effect: DVBE =-aDVCE
And it gets even more complicated (e.g.,
Miller effect, etc…
Clever circuit designers take advantage of these
complexities, or cancel them out (e.g., with
feedback).

## Slide 20: Simplest 1-transistor circuits
Fixing or floating various terminals gives various circuit properties (and a whole lot to remember and get confused about), e.g.,
fixed
out
in
out
fixed
fixed
Switch
in
out
fixed
in
Follower
Current source (sink)
Amplifier
out
fixed
fixed
R1
R2
G = -R1/R2
i = Ve/R
Zout = Zin/b
iout < biin
From these 4 abstractions we built

## Slide 21: 2-transistor circuits

## Slide 22: Which familiar circuits do you see?
Knowing 1 & 2 transistor circuits allows you to visually parse and understand more complex ones

## Slide 23: Which familiar circuits do you see?
Knowing 1 & 2 transistor circuits allows you to quickly visually parse and understand many more complex circuits
Differential amp
Current
mirror
Current
mirror
darlington
darlington
darlington
Current
sink
Switch/regulator
Voltage dividers
Learn to see higher level, more abstract semantic elements

## Slide 24: Electronics jargon and terms
Voltage – D in electric potential between 2 points in a circuit …
Current – flow of + charges
Impedance – a measure of opposition to current, =V/i
Reactance – imaginary part of impedance
AC/DC -- rock band
Ripple – residual AC on a DC voltage
Stiff – ability of a source to maintain its voltage under varying current (low “droop”)
Compliance – voltage range over which a current source is constant
Bypass – capacitor || a resistor to bypass AC frequencies
Amplifier – a device that changes the amplitude of a signal
Gain – ratio of output/input
Clipping – nonlinear distortion from saturation of an amplifier
Filter – a device that removes part of a signal
hFE or b – BJT current gain
Biasing – lit. “to push off center” setting quiescent conditions to improve circuit behavior
Quiescent – condition or state without input (lit. quiet)
Bootstrap – getting a circuit to turn on in the proper state
Transconductance – Diout/DVin

## Slide 26: FETs
7-2

## Slide 27: How the n-FET works
Conduction between Source and Drain is controlled by E field between Gate and substrate
  Conduction can be bidirectional (no diode)
  4 terminal device, though generally substrate connected to S or D
  ~zero DC gate current (Rgate ~1014ohms)

## Slide 28: n-MOSFET vs. BJT
Higher VGS ~2V
Less Early effect
Drain formulas:
where
k a T-3/2
VT =“gate threshold”
~1.5-2V
One gripe I have about Boysen & Kybett is they don’t include characteristic curves

## Slide 29: Types of FETs
N or P
x
Enhancement or depletion
x
junction or oxide
= 8 possibilities
4 are common

## Slide 30: Applications
FET switch controls bulb with ~0 gate current
Most things you can do with a BJT can be done with FETs.
  FET’s high Zin is good … and bad
  Much more sensitive to electrostatic discharge (ESD)
    Fig. 3.50; pg. 170; last slide
  Parasitic capacitances (Fig. 3.44) reduce Z and switching time
  CDS can cause “feedthrough” (Fig. 3.45) and glitches (Fig. 3.48)

## Slide 31: CMOS: “Digital Abstraction”
Note: FET is conducting when E = -DV across the gate-substrate is parallel to arrow
CMOS logic inverter (“NOT”) is push-pull configuration
CMOS NAND and OR gates
  Theorem: ANY logic function can be made by combining NAND, OR, and NOT
  Note: Current only flows during switching
=A+B
open circle indicates inverter
Z=AB
= Vin

## Slide 32: State of the art
Intel Core i7 packs 731 million transistors in 263mm2 and costs $few hundred (~25k transistors per penny)
  Old data, 3.2 billion on the same die now : https://en.wikipedia.org/wiki/Transistor_count

## Slide 33
10/21 – M1Pro = 33.7B transistors at 5nm
M1Max = 57B
M1Ultra = 114B
6/22 – M2 Pro = 40B @ 5nm
M2 Pro Max = 67B @ 5nm
  https://en.wikipedia.org/wiki/Moore%27s_law#Recent_trends

## Slide 34
5 watts
125 watts

## Slide 35: Transistor dimension evolution
Apple M1 = 5nm

## Slide 36: Transistor dimension evolution
TSMC
5nm
171.3

## Slide 37: Diminishing returns

## Slide 38: What’s the future??
Short term, Moore’s law is hanging on:
  https://sparrowsnews.com/2020/07/13/tsmc-2nm-process/
Not just in electronics, we have to expect the future won’t be like the past …
Change can occur smoothly or in jumps …
We live in interesting times …

## Slide 39: ESD techniques
FETs design makes them extremely sensitive to static electricity
  Discharge from your finger on a gate can easily and invisibly destroy the device
Always discharge static electricity from your body and tools through a low Z ground (and avoid charging up)
Keep a hand touching the chassis
Touch chassis before touching parts
Keep parts in conductive bags, conductive foam, or tin foil
Use grounded soldering iron and solder (Note: float iron if soldering “hot” circuits.
Wear a grounded wrist strap
Be extra careful when the Santa Ana winds are blowing
…

## Slide 40: Wrap up
FET’s can do what BJTs do, and in some ways do it better
While BJTs are common as discrete devices, FETs and CMOS in particular dominate very large scale integrated circuits (VLSI)
CMOS is very energy-efficient because it only draws current during switching
  This is the sinew of all our CPUs, GPUS, and computers, and whole families of integrated circuits
  Welcome to the digital abstraction: CMOS FETs in 2 saturation states representing Boolean logic states of 0 and 1
Use care to eliminate ESD in FETs

## Slide 41: Feedback LED regulator
Feedback is one the most important concepts in electronics
D5 connects to an Arduino PWM output, which turns on the MOSFET Q2 when VG >~2.5V
Turning on Q2 makes RDS <~ 0.8W resulting in a current through the LED D1 and R3.
When iD1 ~ 0.6V/R3, the BJT Q1 begins conducting, pulling current from D5 through R1, thereby lowering VG  VD5 - ic*10k.
When VG drops to ~2.5V, Q2 increases its RDS lowering iD1 …
Stability is achieved via this negative feedback for iD1 ~ 0.6V/2W ~ 300mA (this is a high-power LED).
Questions:
What do the 10k and 4.7uf on right side do?
Why didn’t V (at the top) matter?
Notes: What does each component do?

## Slide 42: Feedback current regulator
Arduino program swept through PWM values, measuring average current on A0
A0 < 1 ADU for PWM < 10, so I measured by hand, with a 4.5-digit DMM
 Able to vary LED current from ~ 5mA – 500mA with PWM = 1-255!!
Notes: What does each component do?

## Slide 43: Reflections …
Like with an LED, always use a series resistor (or other mechanism) to limit a BJT’s base current
  That resistor also enables easy measurement of ib
  You can’t easily tell the state of the transistor by measuring base voltage … E.g., for the 2N3904, VBE hardly changes (~.65-.7) as Ic changes from 1-10mA
BJT’s are current devices: iB controls iC
External Rc often limits iC < hfeiB
FETs are controlled by gate voltage; gate current is practically zero

## Slide 44: CdS photoresistors
Among your components are some CdS photoresistors1
Create an LED nightlight powered by 10V that turns on in the dark and stays off in the light
  Characterize the CdS resistor using your ohmmeter (multimeter on ohms scale), and observing how its resistance changes with light
  A transistor switch turns on when Vb ~ 0.65V (measure it, since ib = 0 for Vbe < the diode’s Vf)
  Design and validate the circuit with a CdS photoresistor to achieve the desired transistor switching behavior: LED off in light, on in dark
  Hints: 1) it maybe easier to first make the opposite – LED turns on with light; 2) Voltage divider equation
1 https://en.wikipedia.org/wiki/Photoresistor

## Slide 45: What next?
Automate control of the LM317
  So the Arduino can effectively turn the R2 knob
  We will control the LM317 voltage via our keyboard and Matlab scripts
  Matlab will communicate directly with the Arduino
Explore AC … time varying voltages and signals, for the rest of the semester
  Build a function generator
  Construct an oscilloscope (in software) to display time-varying signals
  Automate control of function generator’s frequency
We’ll mix up 1 and 2 … we’ll need some AC concepts to do 1.