## Slide 1: Transistors
5-2
First transistor, 1947, Bell Labs
Week 5

## Slide 2: Sierra 2111 schedule
Sierra 2111 is available TTh 1:30-4:30pm, and you’re welcome to attend the class there
Other current events:
  Global climate strike https://fridaysforfutureusa.org/sept-23/, https://twitter.com/ycstrikeLA
  Amanda Gorman opens UN General Assembly
    https://www.youtube.com/watch?v=wW6hoiyYiUI

## Slide 3: Transistor switch circuit
A BJT transistor switches on when Vbe > ~0.6-.7V so we need to reduce the voltage of our LM317 power supply  voltage divider
The collector is powered from the Arduino’s 5V, so only the base voltage (and current) are independent variables
Base current = (A2-A1)/10kW
A0 measures collector voltage

## Slide 4: BJT Golden Rules
There are no golden rules … there are many configurations and possibilities with BJTs…
The base-emitter often acts like a diode
  If Vbe < ~0.6V then ic ~ 0 and the transistor is “off”
  If Vbe~0.6-0.7V (forward biased diode), the collector-emitter conducts
  Making Vbe>0.7V will likely destroy the device quickly
If not saturated, ic = hfe * ib
The transistor will lower its collector-emitter voltage in order to satisfy (3.) But it can’t go below Vce~ 0.01-0.3V
Like diodes (e.g., LEDs), external components are generally needed to limit base and collector currents at safe (for the device) values
…

## Slide 5: Saturation
>> indx = ic < .006;
>> p = polyfit(ib(indx), ic(indx), 1)
ans =
331.0971 0.0037
>> mean(ic(~indx))
ans =
2.2285
>> (Vref-min(data1(:,3)))/2
ans =
2.2550
Rc = 2kW saturated ic at 2.23mA, with VCE = 0.23V – the transistor couldn’t go lower

## Slide 6: What happens in saturation?
“Transistor man” adjusts a variable resistor that’s a voltage divider with Rc. Once set to its minimum value (R=Vce/ic), it can’t go any lower
ic is now saturated at (Vcc-Vce)/Rc, additional increase in ib cannot increase ic
In saturation, the external collector circuitry (Rc) determines ic, not hfeib.
Rc
Vcc
How do you feel about this model?

## Slide 7: Design Challenge
Objective: Make an LED night light that automatically turns on in dark, and turns off in light
Methods:
  Characterize a CdS photoresistor (https://en.wikipedia.org/wiki/Photoresistor)
    Use your ohmmeter to measure its resistance under light and dark conditions
  Design a transistor switch to turn on/off an LED based, controlled by the CdS photoresistor
  Prototype and test (and iterate) – remember, that design is more of a circular or spiral process than a linear one